## Slide 1
VNM HANDBRAKE V1.5
Quick Guide
1. VNM Handbrake V1.5 body
2. Red (stiffest), blue (stiffer) springs
3. Allen key set
4. USB A male – GX12 male cable
5. Handle
6. Handle extension
7. 0-90 degree conversion adapter (2 pcs)
2
3
4
5
6
1
7
X2
On the left side of the Handbrake: XH2.54-4P port for load cell connection
VNM Handbrake V1.5
Designed by VNM Simualtion
Made in Vietnam
On the right side of the Handbrake is:
Switch DFU/Game Mode
Slide left side to select DFU Mode or right side to select Game Mode
DFU RUN
At the bottom of the Handbrake: GX12 female port
Content
Connection
Adjust Spring & elastomer:
Twist the threaded cap:
Clockwise: Heavier pull force
Counter-clockwise: Lighter pull force
Adjust the angle of inclination:
Remove the 2 bolts on both sides
Pull out the endstop part
Choose the angle of inclination by rotating the endstop part
Push the endstop part in the sliding slot
Tighten the bolts.
+
_
Adjust Handbrake
Choose the appropriate handle height
X1
X1
X2
M5x10
X4
X6
M5x12
M5x10
X4
X5
X1
M5x20
VNM Handbrake V1.5 set up for 90 handle
Handbrake V1.5 set up for 0 handle
7 angle options
Choose the appropriate angle/inclination
90
75
60
45
30
15
0
Set up

## Slide 2
Remove bolts
OR
Tighten bolts
Remove bolts
Tighten bolts
Blue spring
Red spring
Mounting Drawing
Exchange Spring
Clamps Size